Part No. T0297, Rev A

December 2009

Page 1 of 2

Vanguard Networks 3400 Series

Software Advisory Notice

Bootprom Release 1.06

# 1.0 Introduction

This notice contains information about a new version (1.06) of the 3400 Boot prom which is being factory installed starting December 2009.  The changes introduced will make the software upgrade process more robust and streamline operations.

Two features introduced with this new 1.06 version are:

- Fix for CR17962, which caused the node not to boot from alternate image, if current image is corrupt.  The unit will now recover and boot to alternate image, providing that “best practice” is always followed, that is, ensuring an alternate image was previously loaded into the 3400.

- TFTP coldload capabilities via the “ZAP” menu.  This will allow the customer to TFTP image load if the current/running image gets corrupted and the 3400 CTP displays the “Please send coldload” message.

The new bootprom can be downloaded from the Vanguard Networks web site:

http://www.vanguardnetworks.com/support-downloads-boot-proms.htm

This notice supplements the updated Vanguard Applications Ware 7.2R00A Software Release Notice (Part Number T0284-01 Rev D Dec 2009) which can be downloaded from the Vanguard Networks web site: http://www.vanguardnetworks.com/Collateral/Documents/English-US/R7-2-Software-Release-Notice-RevD-12-4-09.pdf

# 2.0 Boot Prom and Cold loader Matrix Upgrade

A new version (1.06) of the 3400 Bootprom is being factory installed starting December 2009.    To load the new Bootprom reference the Vanguard Software Loader Manual Part No T0057 Rev V, this can be downloaded from the Vanguard Networks web site:  http://www.vanguardnetworks.com/Collateral/Documents/English-US/057.pdf

If you are running 7.2.R00A or earlier the bootprom file must be placed in the “C:\Vanguard\SFW_IMGS\3400\Coldload\Bootprom” directory on your PC in order for the Vanguide Software loader to automatically detect and load this new version.

The following tables describe the valid combinations of released flash image, boot code, on-board flash, flash SIMM and DRAM for the Vanguard 34xx platforms. In the following table, the Status column can be Valid, Invalid and VR (Valid and Recommended). “Valid” means that the router is basically working, but some functionalities such as an option feature support, might not be available. “Invalid” means that the router is not working with such a combination. “VR” (Valid and Recommended) means that the combination is valid and recommended to use according to our current knowledge.

Vanguard 3400 Boot prom, Coldloader and Image Matrix

| No. | Release | Boot Code Version | Cold-loader from Release | On-Board Flash | Flash SIMM | Status | Comment |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 7.0.P12A or earlier | 1.04 | 7.0.P12A | 16M | None | Valid | None |
| 2 | 7.1.R00A | 1.05 | 7.1.R00A | 16M | None | VR | 64k CMEM, 4M image maximum |
| 3 | 7.2.R00A | 1.05 | 7.2.R00A | 16M | None | VR | 64k CMEM, 4M image maximum |
| 4 | Factory Installed or from WWW.Vanguardnetworks.com | 1.06 | 7.2.R00A | 16m | None | Valid | 64k CMEM, 4M image maximum |

Notes:

3400 Series Platform

- The installed 3400 SDRAM is 64Mbytes.

Reference Applications Ware Software Release 7.2.R00A Release Notice Part No. T0294, Rev. D Dec 2009  which can be found at:  http://www.vanguardnetworks.com/Collateral/Documents/English-US/R7-2-Software-Release-Notice-RevD-12-4-09.pdf